### Network Scaling
There can only be one OpenLCB service provider on a network using Bonjour.

The config tool, other software and local hubs connects to the OpenLCB service. The software gets an OpenLCB node number allocated by the connection to the OpenLCB service. Only the OpenLCB service provider hub needs to do any filtering.

Local hubs are used for CAN gateway connections, they use the same software as the OpenLCB hub, but don't register the service, don't need to filter, and don't need to allocate nodenumbers. It needs a configuration option to switch to local mode otherwise the order of power up decides the roles. Also configuration options to allocate node numbers to gateways and to enable gateways to connect to the hub on the same machine and not on a remote machine.
### Small network of up to 50 nodes.
 PC for configuration not normally connected. Runs the config tool, hub and gateway code.

CAN Segment with up to 50 nodes
OpenLCB Hub

Gateway
USB/CAN
Config
Tool
Notebook PC

### Medium network of up to 200 nodes.
Single board low cost or old PC used as a hub, could also run the config tool. Wireless access point and WiThrottle or similar software optional.

Notebook PC

Ipod Touch

Config
Tool
Wireless
Throttles etc.
Low cost
 single board

OpenLCB Hub

Gateways
USB/CAN

### Large network of up to 1000 nodes.
Up to 5 low cost hubs, one acting as the OpenLCB service provider.

OpenLCB Hub

Config
Tool

Wireless
Throttles etc.

Notebook PC
Ipod Touch

Low cost
 single board
Local
Hub

### Huge network of up to 10000 nodes.
Up to about 50 connections to the OpenLCB hub machine, 4 CAN connections to each local hub, up to 50 nodes per CAN segment.

OpenLCB Hub

Local
Hub
Local
Hub

Local
Hub

Config
Tool

Wireless
Throttles etc.

Server
Notebook PC
Ipod Touch